## Slide 1: TLRISC-V Design Spec
Created by TuanLa
Designing RISC-V RV32I

## Slide 2: Overall

## Slide 3: Overall

## Slide 4: Overall

## Slide 5: Conventions
Naming: <master>_<slave>_<signal>
Naming: <stage>_<signal>
Enable of Pipeline FFs (except vld FFs): CEN = (!stall & vld); // vld here is for power saving
Valid FFs: CEN = !stall; // When vld = 1’b0 (flusing), the pipeline still runs.

## Slide 7: IF

## Slide 10: Instructions

## Slide 11: Overview Design

## Slide 12: REGFILE: Registers File
31x32-bit reg (r1-r31) + r0 (always = 0) + 1 PC

## Slide 13: RAM Controller
Write to RAM: wadd, wdata[31:0], wenb
Read from RAM: radd, rdata[31:0]
Write: always write from MEM.
Read: either from MEM or IF. First come first serve!
Busy signals to MEM and IF.

## Slide 14: RAM Controller
MEM read has higher priority than IF read. (downstream needs to be released)
Request then get data after 1 clock cycle.
MEM write will always be processed.

## Slide 15: IF: Instruction Fetch
IF always requests each cycle so no need for REQ signal!
Only busy signal from RAM is required!
For Fetching Instruction from RAM:
In: RAM_IF_rdata, RAM_IF_busy
OUT: IF_RAM_radd
It DOESN’T have branch delay slots!
PC is intercepted when: branch or jump.
For other blocks:
In: EX_IF_pcupdate, EX_IF_pcnew
Out: IF_pc, IF_inst, IF_vld
For flushing:
In: EX_flush
Common signals: clk, rst

## Slide 16: ID: Instruction Decode
Only decode when receiving valid signal from IF.
Opc = inst[6:0]
Rd= inst[11:7]
Imm[0] = (i-type) ? Inst[20] : Inst[7] // s-type
Imm[4:1] = (s-type || sb-type) ? inst [11:8] : inst [24:21] // i-type or uj-type
Imm[10:5] = inst[30:25] // i-type or s-type or sb-type or uj-type
Imm[11] = (i-type || s-type) ? Inst[31] : (sb-type) ? Inst[7] : inst[20] // uj-type
Imm[12] = (sb-type) ? Inst[31] : inst[12] // u-type or uj-type
Imm[19:13] = inst[19:13] // u-type or uj-type
Imm[20] = (u-type) ? Inst[20] : inst[31] // uj-type
Imm[31:21] = inst[31:21] // u-type
Rs1 = inst[19:15]
Rs2 = inst[24:20]
Funct3 = inst [14:12]
Funct7 = inst [31:25]
Inst[1:0] is set to 2’b11 as in base ISAs
Remain space is for extension

## Slide 17: EX: Execute
Computation:
  Add/Subtract by Registers/Immediate
  Logical/arithmetic left/right shift by Registers/Immediate
  Bitwise AND/OR/XOR by Registers/Immediate
  Comparison by Registers/Immediate
  Load/Add PC
Branch - Jump:
  Branch if equal/not equal/less-great signed/less-great unsigned
  Jump and link
Mem access:
  Load/Store
  Fences?

## Slide 18: EX: Execute – Branch Taken + Flush
Output: EX_IF_pcupdate, EX_IF_pcnew
Input: EX_pc, EX_opcode, EX_rs1_val, EX_rs2_val
Flush objective: clear previous pipeline reg
Flush behavior: keep in 1 cycle, after that release.
rd will be written when flushing.
Flush signal == PC_update signal

## Slide 19: EX - Comparator
Spec:
  Input: two 32-bit registers, signed/unsigned signal
  Output: less than, equal, greater or equal than

## Slide 20: EX - Data Hazard Controller
This controls the reading of register file for 2 operands.
It prevents:
  Operands are updated from previous adjacent instruction -> Solution: keep rd, no need to stall anything.
  Operands are taken from MEM of the previous instruction -> Solution: add bubble, need to wait data from MEM.
Inputs: EX_rs1, EX_rs2, EX_rd, MEM_rd, MEM_rd_val, EX_opcode
Outputs: EX_rs1_val, EX_rs2_val, EX_busy